Form No.:

Hollow Concrete Block Test Requisition Record

Project: 			Contract No.:

Site: 			Client/ Implementing Agent:

Contractor: 			Supervisor:

| Concrete | Source (sampled) | (Tuck mixer/ Batch plant/ Mixer/ Supplier/ etc.) |
| --- | --- | --- |
|  | Class |  |
| Test purpose | Mix design (trial mix) |
|  | Periodic check – compression test @ 4,000 pcs. |
| HCB used for | (mention the proposed use and location) |
| Cement type |  | Cement source |  |
| Aggregate (Type) | Coarse |  | Aggregate (source) | Coarse |  |
|  | Fine |  |  | Fine |  |
| Testing laboratory |  |

HCB samples were made in accordance with

| ES | BS | ASTM | Others |
| --- | --- | --- | --- |

| Mix proportion | Cement: | Sand: | Agg.01: | Agg.02: | Red ash: | Water: |
| --- | --- | --- | --- | --- | --- | --- |

| Box size (cm³): | Method of compaction: | Vibrator | Hand |
| --- | --- | --- | --- |

HCB test specimen data

| Test ID | Specimen dimension | HCB sample | Total No. of HCB |
| --- | --- | --- | --- |
|  | L x W x H (m) | Prod. date | Prod. Time | Prod. Temp. | Age | Slump |  |

Condition of HCB specimen

| good | poor compaction | honey comp | bad dimension |
| --- | --- | --- | --- |

Condition of specimen sent to laboratory

| Confined (with moist sand) | Bare |
| --- | --- |
| Sample submitted by | contractor | consultant | other |
| Sampled by (the contractor or MHE) Name Date & signature | Recorded by (consultant – MHE) Name Date & signature | Approved by (GTZ-IS) Name Date & signature |

Form No.:

Hollow Concrete Block Test Approval Record

Project: 			Contract No.:

Site: 			Client/ Implementing Agent:

Contractor: 			Supervisor:

| Concrete | Source (sampled) | (Tuck mixer/ Batch plant/ Mixer/ Supplier/ etc.) |
| --- | --- | --- |
|  | Class |  |
| Test purpose | Mix design (trial mix) |
|  | Periodic check – compression test @ pcs. |
| HCB used for | (mention the proposed use and location) |
| Cement type |  | Cement source |  |
| Aggregate (Type) | Coarse |  | Aggregate (source) | Coarse |  |
|  | Fine |  |  | Fine |  |
| Testing laboratory |  |

HCB Test Result Data

| Test ID | Specimen dimension | HCB | Average Min Tot |
| --- | --- | --- | --- |
|  | L x W x H (m) | Date produced | Date tested | Age | Unit weight | Compressive strength |  |

HCB Test Result & Specified values

| Description | Unit | HCB test result | Specified values |
| --- | --- | --- | --- |
|  |  |  | Class A (load bearing walls) | Class B (load bearing) | Class C (non- load bearing) |
| Avg. 28 days result | Mpa |  | 42 kg/cm² | 35 kg/cm² | 20 kg/cm² |
| Individual 28 days result | Mpa |  | 38 kg/cm² | 32 kg/cm² | 18 kg/cm² |
| Slump | mm |  | < 30mm | < 30mm | < 30mm |
| Water cement ratio | % |  | < 58% | < 58% | < 58% |
| Max. aggregate size | mm |  | 10mm | 10mm | 10mm |
| Cement content | Kg/m³ |  | > 340kg | > 300kg | > 250kg |

Note:	1) Test records & Data sheets should be attached

2) Avg. total & minimum values of HCB should be calculated as per EBCS

| Comment/ instruction by the consultant (if any) |
| --- |
| Sampled by (the contractor or MHE) Name Date & signature | Recorded by (consultant – MHE) Name Date & signature | Approved by (GTZ-IS) Name Date & signature |

Attachment No.: 002

- Hollow Concrete Blocks (HCB):

  - Classification:

Hollow concrete blocks are classified into the following classes:

- Class A and B are load bearing HCB units and suitable for

      - External walls pointed, rendered and plastered

      - The inner leaf of cavity walls or stone masonry

      - Internal walls or partitions

      - Panels in steel framed and reinforced steel framed buildings

- Class C are non- load bearing HCB units and suitable for

      - Non- load bearing internal panels in steel framed and reinforced concrete buildings

  - Mixing proportions for HCB production:

The following mixing proportions for the production of hollow concrete blocks are used in accordance to ESC D3.301:

Table 1

| Class | Proportions by volume of |
| --- | --- |
|  | Sand | Gravel 00 | Gravel 01 | Red ash or pumice | Cement |
| A | 2 | 1 | 1 |  | 1 |
|  | 2 | 1 |  | 1 | 1 |
| B | 2 | 1 | 2 |  | 1 |
|  | 2 | 1 |  | 2 | 1 |
| C | 3 | 1 | 2 |  | 1 |
|  | 3 | 1 |  | 2 | 1 |

  - Dimensions:

The nominal dimensions of HCB are indicated below:

Table 2

| Width (b) (mm) | Height (h) (mm) | Length (l) (mm) | Face shell (d) (mm) | Web (e) (mm) | Weight (kg/m³) |
| --- | --- | --- | --- | --- | --- |
| 100 | 200 | 400 | 20 | 20 | 1,200 |
| 150 | 200 | 400 | 25 | 25 | 1,200 |
| 200 | 200 | 400 | 30 | 25 | 1,200 |
| 250 | 200 | 400 | 35 | 30 | 1,200 |
| 300 | 200 | 400 | 40 | 30 | 1,200 |

However, the dimensions used in the University Capacity Building Program differ from the nominal dimensions, and are shown below:

Table 3

| Width (b) (mm) | Height (h) (mm) | Length (l) (mm) | Face shell (d) (mm) | Web (e) (mm) | Weight (kg/m³) |
| --- | --- | --- | --- | --- | --- |
| Full blocks |  |
| 90 | 190 | 390 | 20 | 20 | 1,200 |
| 190 | 190 | 390 | 30 | 25 | 1,200 |
| Half blocks |  |  |  |  |
| 90 | 190 | 190 | 20 | 20 | 1,200 |
| 190 | 190 | 190 | 30 | 25 | 1,200 |

  - Minimum compressive strength:

The minimum compressive strength for HCB according to ESC D3.301 is indicated below:

Table 4

| Class | Average of 6 HCB | Individual HCB |
| --- | --- | --- |
|  | Mpa | kg/ m³ | Mpa | kg/ m³ |
| A | 4.2 | 42 | 3.8 | 38 |
| B | 3.5 | 35 | 3.2 | 32 |
| C | 2.0 | 20 | 1.8 | 18 |